## Slide 1
WHAT IS RDS/RBDS?
The European Broadcasting Union (EBU) first introduced the official RDS specification in March 1984 after nearly a decade of development.
The United States officially adopted its own version, called RBDS (Radio Broadcast Data System), on January 8, 1993, though the technical standard framework was completed by the National Radio Systems Committee (NRSC) in late 1992.
tylerwoodward.me
tylerwoodward.me

## Slide 2
WHAT DOES RBDS DO?
It puts data on your FM signal. Your radio reads it and shows you things — the station name, what song is playing, the format, the time. It's how your car knows you're listening to WLCW instead of just seeing "100.1."
It does this by piggybacking 1,187.5 bps of data on a 57 kHz subcarrier -- silent, automatic, and invisible until something breaks.
tylerwoodward.me
tylerwoodward.me

## Slide 3
TOO LOW, TOO HIGH, AND THE SWEET SPOT...
RDS Injection Level
RDS rides on a 57 kHz subcarrier -- exactly 3x the 19 kHz stereo pilot, phase-locked to it. Injection level is how much of your total FM modulation budget the RDS subcarrier consumes. It counts against your composite headroom just like audio does.
tylerwoodward.me
tylerwoodward.me

## Slide 4
Too low (below ~2%)
Sweet spot (2-4%)
Too high (above ~5%)
TOO LOW, TOO HIGH, THE SWEET SPOT
RBDS INJECTION
WHAT HAPPENS?
Decode errors, intermittent group loss, receivers that catch RDS for a few seconds then drop it. PI lookups fail silently.
Clean decode on virtually all receivers. Reliable group delivery. PI code stable. IEC 62106 and NRSC both land here.
Eats into audio modulation headroom. Can cause composite clipping if your processor isn't accounting for the subcarrier load.
tylerwoodward.me
tylerwoodward.me

## Slide 5
TOO LOW, TOO HIGH, THE SWEET SPOT
RBDS INJECTION
tylerwoodward.me
tylerwoodward.me

## Slide 6
PS
PTY
RT
PI
AF
RT+
RDS Data Fields
What Each One Does
Program Service
8-character station name on the radio face.
Static. Don’t scroll it.
Group 0A/0B
Program Type
Format code (Rock, News, Country...).
Don't leave it at 0.
All Groups
RadioText
Now-playing text up to 64 chars. Artist
- Title. Updates each song.
Group 2A
Program ID
4-digit hex station fingerprint. Used by RadioDNS & AutoStage. Never change it.
All Groups
Alt Frequencies
Translator list for auto-retuning on a drive. Bad AF = retunes to dead air.
Group 0A
RadioText+
ODA extension that tags what each part of RT is (title, artist, album, station name).
Group 3A + ODA
tylerwoodward.me

## Slide 7
M/S
TP
CT
TA
PTYN
DI
RDS Data Fields
What Each One Does
Music/Speech
1-bit flag. Lets receivers adjust EQ. Set it correctly for your format.
Group 0A/0B
Traffic Programming
Set to 1 if station carries traffic programming.
All Groups
Clock Time
UTC clock, fires once per minute. Only transmit if it's accurate.
Group 4A
Traffic Announcement
Active traffic announcement. Auto-switching discouraged in the US.
Program Type Name
PTYN stands for Program Type Name. It allows a radio station to display a customized, 8-character description of their music genre
Group 3A
Decoder Information
A 4-bit signal that tells your radio how to dynamically process the audio coming from the station
Group 0A/0B
Groups 0A, 0B, 14B, 15B
tylerwoodward.me

## Slide 8
0A
2A
3A
12A
What is 4BD7?
It is a "Free Format" group: In the official RDS specifications, Group 12A is originally left blank for custom applications. When Group 3A broadcasts the AID code 4BD7, it tells your radio to specifically use Group 12A for RT+
The AID code: The label that says, "This package contains Radio Text Plus data; open it using your RT+ software."
Group Allocation
What Those Percentages Mean??
The Workhorse
PS: Program Service
AF: Alternate Frequency
TP: Traffic Programming
TA: Traffic Announcement
MS: Music or Speech
Sends 4 times every second
RDS transmits at 1,187.5 bps. The percentages show how much of that fixed bandwidth each group type consumes.
RT (Standard RadioText)
a 64-character text field that allows FM stations to transmit longer alphanumeric messages directly to your radio's display
Sends 3 times every 2 seconds
RT+ Identification Packet
This group acts as the signpost, telling the radio: "Hey, we have RT+ here, and you can find the actual digital tags over inside Group 12A.
Sends every 10 seconds
RT+ RadioText+ Tagging
While Group 2A sends the actual text ("Blinding Lights by The Weeknd"), Group 12A sends the invisible binary codes that say: "The title starts at letter 14 and is 15 letters long".
Sends every 2 seconds
Common failure: TMC/EON default-on with nothing feeding them → OA and 2A get starved → PS sluggish, RT lags 20-30 sec. Fix: switch off unused groups.

## Slide 9
RT+1
RT+2
RadioText+
RT+1 & RT+2
RT+1
Common RT+ Content Type Codes
The software in your screenshot uses these fixed numeric identifiers to understand what it is displaying:
  1 = Item.Title (Song Name)
  2 = Item.Artist (Performer)
  3 = Item.Composition (Composer)
  4 = Item.Movement (Classical music section)
  32 = Station Name Long (As seen on your screen)
Why is RT+2 Empty?
Stations use RT+1 for single items like station slogans (code 32). The RT+2 box stays empty because there is no second metadata type to tag. When a song plays, the encoder uses both slots simultaneously: RT+1 switches to code 1 (Song Title) and RT+2 switches to code 2 (Artist Name).
tylerwoodward.me

## Slide 10
PTYN
Program Type Name
A Little Extra...
Program Type Name
  If the station wants to be more specific than just "Top 40", they can use the PTYN field to broadcast a custom nickname (e.g., HITLIST, CHR, or LIVE MIX)
  It is optional: If a station is perfectly fine with the default label "Top 40", they can leave PTYN completely blank.
  The Data Envelope: PTYN information is transmitted over the inside Group 10A.
  Display Only: Car stereos cannot use the custom PTYN text for automatic tuning or station searching; it is purely visual eye candy for your dashboard.
tylerwoodward.me

## Slide 11
0 | None | 16 | Rhythm and Blues (R&B)
1 | News | 17 | Religious Music
2 | Information | 18 | Religious Talk
3 | Sports | 19 | Personality
4 | Talk | 20 | Public
5 | Rock | 21 | College
6 | Classic Rock | 22 | Spanish
7 | Adult Hits | 23 | Talk (Spanish)
8 | Soft Rock | 24 | Hip Hop / Rap
9 | Top 40 (CHR) | 25 | N/A
10 | Country | 26 | N/A
11 | Oldies | 27 | N/A
Program Type
It tells your car or home stereo exactly what kind of content is currently broadcasting.
tylerwoodward.me

## Slide 12
12 | Soft | 28 | N/A
13 | Nostalgia | 29 | Weather
14 | Jazz | 30 | Emergency Test
15 | Classical | 31 | EMERGENCY ALERT (EAS)
Code 31 (Emergency Alert):
This code is highly protected. When triggered, it forces your car stereo to instantly switch away from your CD, Bluetooth, or auxiliary audio input to broadcast the local Emergency Alert System (EAS) audio.
In the United States, almost no one uses PTY Code 31 anymore.
Because it acts as a "forced hijack," if an engineer accidentally misconfigures a radio station encoder and leaves Code 31 running, it will freeze every car stereo within a 30-mile radius onto that station. Fearing massive FCC fines for disrupting consumer equipment with accidental false alarms, most stations permanently disable the code in their automation software.
Program Type
It tells your car or home stereo exactly what kind of content is currently broadcasting.
tylerwoodward.me

## Slide 13
Last Two Nibbles
Second Nibble
First Nibble
Country code. The US spans multiple country code values across states and regions in the IEC 62106 system - it's not a single digit for the whole country.
Area coverage code. Describes the station's broadcast footprint - local, regional, national, etc.
Program reference number. The station-specific part. For US stations this is calculated from call letters per the NRSC-4-B algorithm.
4 bits
4 bits
8 bits
The PI Code
A 16-bit value displayed as 4 hex characters (e.g., 1965). It's the station's unique fingerprint in the entire RDS ecosystem. It rides in every single RDS group, not as a separate transmission
How It Works and Why It Matters Downstream
tylerwoodward.me

## Slide 14
tylerwoodward.me

## Slide 15
Your Call Letters, In Hex
739C isn't a random number. It's WLSU, expressed in hex.
Get this wrong and your translators retune to the wrong station, your AF list breaks, and your RadioDNS lookup goes nowhere. Every system downstream depends on this one code being correct
https://picodes.nrscstandards.org
tylerwoodward.me

## Slide 16
What is AF?
A list of up to 25 frequencies that carry the same programming. Your main signal plus any translators. Stored in Group 0A and broadcast continuously.
tylerwoodward.me

## Slide 17
PI Code: 1313
PI Code: 1313
PI Code: 1313
When signal strength drops, the receiver doesn't just jump to the next frequency on the AF list and hope for the best. It tunes there quietly in the background, checks the PI code, and only switches if it matches. The listener never hears it happen.
AF is the first place a wrong PI code costs you listeners. RadioDNS and DTS AutoStage are the next two.
tylerwoodward.me

## Slide 18
PI
That PI Code
4 hex digits.
Your station's identity.
RadioDNS
our PI code and frequency become a DNS lookup. The receiver uses it to find whatever internet services your station has registered — metadata, logos, program guides. Wrong PI code, the lookup goes nowhere.
DTS AutoStage
The car reads your PI code, sends it to Xperi's platform, and gets back album art and station branding. Wrong PI code means no match — plain text or someone else's content on the display.
*all without HD Radio
tylerwoodward.me

## Slide 19
THE CARS ALREADY LISTENING FOR IT
WHO SUPPORTS WHAT?
RadioDNS
BMW
Audi
VW Group
DTS AutoStage
BMW
Audi
VW Group
Mercedes-Benz
Ford
Hyundai, Kia, and Genesis
Tesla
Proprietary / RDS only
GM
tylerwoodward.me

## Slide 20
YOU HAVE TO GIVE IT INPUT LIKE JOHNNY 5
THE ENCODER DOESN'T KNOW WHAT'S PLAYING
Middleman Software
BE TREplus
MetaRadio
Xperi RAPID
ENCO PADapult
Pira MagicRDS
Playout System
HTTP, XML feeds, file-based polling, and UDP
RBDS Encoders
(External and TX)
Inovonics
Omnia
Nautel
GatesAir
DEVA
WorldCast Systems (Audemat)
Pira
WorldCast Ecreso FM
Rohde & Schwarz
UECP over TCP/IP, ASCII over
TCP/IP, HTTP POST / GET,
and RS-232/Serial
Satellite Receiver
On-Air Staff Input
API, TCP/IP, or Serial/FTP
Web Browsers
(Firefox, Edge, Chrome, etc)
tylerwoodward.me

## Slide 21
PI Code
Set correctly per NRSC-4. Never change it. Verify with FCCdata.org. Translators need the NRSC translator PI table.
PS Name
Static. 8 characters. Call letters or brand name. Never scroll it.
RadioText
Dynamic. Artist - Title. Updated on every song change. Both RT and PS -- car displays vary on which field they show.
PTY
Set accurately for your format. Leave it alone. Do not leave it at 0.
WHAT GOOD LOOKS LIKE
BEST PRACTICES
tylerwoodward.me
TP/TA
Only set TP if you actually carry traffic. Never leave TA stuck on.
AF List
List every translator and same-format frequency accurately. Test by driving -- does the radio retune correctly?
Group Allocation
0A: 40-60%. 2A: 20-30% if using dynamic RT. 4A: 5-10%. Disable every group not in use. Check for TMC and EON running by default.
DTS AutoStage
Register your station. Upload logos in all required sizes. Connect automation to push now-playing in real time. Free to participate.
RadioDNS
Host an SI XML file on a public web server. Create the DNS records. Register with RadioDNS. Required for Audi, VW, Porsche, BMW hybrid radio listeners.
Monitor, Monitor!
Inovonics 551 for HD stations. Inovonics 541 for FM-only. RTL-SDR for free spot-checking. RDS doesn't fail loudly -- it just quietly sends wrong data.

## Slide 22
AutoStage works without HD Radio and without RDS (sort of)
AutoStage can fall back to geo-location to identify a station if RDS is absent or broken. But to get the PI-based lookup chain working correctly, the RDS subcarrier has to be present and the PI has to be right. Geo-fallback is a crutch, not a design strategy.
HD Radio PSD does NOT use the PI code
HD Radio has its own PAD/PSD delivery mechanism. The PI code is an FM RDS thing. RadioDNS and AutoStage both need the FM RDS PI. If someone asks 'does HD Radio help with RadioDNS,' the answer is no -- the FM RDS subcarrier has to be there and correct regardless of whether the station has HD.
Most US stations do NOT use RBDS for EAS
The capability exists in the spec. Group 3A can carry Open Data Applications including EAS. The Inovonics 730 + SAGE ENDEC 3644 integration can do it. But the vast majority of US stations are not using it, and most receiver implementations don't act on it.
The listener experience gap is real and visible
A Spotify or SiriusXM stream on the same head unit shows album art, branding, and metadata instantly. An FM station with broken RDS shows a frequency and nothing else. AutoStage and RadioDNS exist to close that gap. Stations that ignore it are choosing to look worse than a streaming service on their own listeners' dashboards.
WRAP UP AND GOTCHAS
tylerwoodward.me

## Slide 23
EXTRA GOODIES
RESOURCES AND LINKS
HTTPS://WWW.NRSCSTANDARDS.ORG/
HTTPS://WWW.RADIOWORLD.COM/RESOURCE-CENTER/RDS-BASICS-BEST-PRACTICES
HTTPS://DTS.COM/AUTOSTAGE/
HTTPS://RADIODNS.ORG/
HTTPS://PICODES.NRSCSTANDARDS.ORG/
tylerwoodward.me